# Phys 481                                                                                           Winter 2012

# Worksheet # 11

Wednesday, February 8, 2012

# Name

Questions (5 pts):

A circular aperture of radius 1 mm is inserted at a distance of 10 cm from a point source emitting light with a wavelength of 500 nm.

- If the observation point P is on the axis connecting the center of the aperture with a point source at a distance of 10 cm away from the aperture, how many zones does the aperture contain?

- How would your result change if you moved the screen further away by 10 cm (along the same axis) ?

Bonus question (2 pts): how many zones would the same aperture contain in the Fraunhofer limit (i.e. large distances from the aperture to the point source and to the observation point) ?