## Slide 1
e-
Photon
The Electromagnetic Spectrum
Ionizing
Bond Breaking
Electronic
Vibrational
Rotation
NMR
MRI
You’ll often see this plot flipped, left to right
Slide 1
High Energy
Low Energy
Visible
“wavenumbers” = 1/λ cm-1
350 nm
650 nm
2500 nm
20,000 nm
Visible
near-IR
mid-IR
4000 cm-1
500 cm-1
High Energy
Low Energy
Tissue is translucent

## Slide 2
Bond Distance and Vibrational Energy
Standard Bonding Representation
Slide 2
Distance
Energy
neg 0 pos
H
Cl
H
Cl
H
Cl
H
Cl
H
Cl
Bond distance
https://www.azom.com/article.aspx?ArticleID=15226
Infrared spectrum of HCl gas
Cl vs
17
35
Cl
17
37
1 / λ (cm-1)
Quantized!
ν = 1/(2π) √k/m
ν : frequency
k: force constant (measure of bond stiffness)
single < double < triple
m: reduced mass – m1m2/m1+m2
~Harmonic oscillator math
Vibrational energy  IR photons
@ absolute zero all motion stops
Vibrational quantum levels
Why start with a gas phase IR spectra???
Bond
energy

## Slide 3
Why P-Chemists Use the Gas Phase:
Ideal Gas Law Assumptions
Slide 3
H2O gas phase
H2O liquid phase
In the gas phase molecules do not interact (assumption)
pure individual molecular vibrations
In the liquid phase molecules are touching
molecular vibrations are modified (change in energy) by interactions with neighboring molecules
In water the highest energy intermolecular interaction is????
H-O
Hydrogen bonded H-O

## Slide 4
What Determines Which Molecules
Absorb Infrared Energy?
H2, N2, O2 do not absorb infrared energy
And CO2, H2O and CH4 all absorb IR?
Why?
Absorbing an IR photon must change the atomic positions in a way that results in a change in the molecular dipole moment
H2, N2, O2 cannot have a dipole
Water does ….
Slide 4
H H
O
H H
O
H H
O
H H
O
Stretching
symmetric
Stretching
asymmetric
Bending
In-plane scissoring
H H
O
H H
O
Twisting
Rocking 1
Rocking 2
All greenhouse gases!!
Or simultaneous combinations of the above

## Slide 5
IR Assignment Rules
Actually More Guidelines Than Rules
Slide 5
http://opening.download/spring-opening.html
Group Region – useful for identifying functional groups
Fingerprint region – difficult to make individual peak assignments but useful if you have a reference spectra for comparison
C N
C C
High Energy
Low Energy

## Slide 6
Single Beam IR with No
Background Subtraction
Slide 6
CO2 gas
H2O vapor
H2O vapor
Source and detector variation with wavelength

## Slide 7
A Series of Benzene Derivative
IR Spectra
Slide 7
H-O
C=O
=C-H
=C-H
>3000
=C-H
H-O
-C-H
<3000
-C-H
C=C
C=C
C=C
C=O

## Slide 8
Building a Spectrophotometer
In the UV/Visible region wavelength selection is accomplished with a monochrometer
And then came the Michelson Interferometer ……
The original “dispersive” IRs had a reasonable similar design
Slide 8
Broad Band White Light Source
Slit Isolates Desired Wavelength
Dispersed Into Discreet Wavelengths
Monochromator
Photomultiplier (PMT) or
Silicon Photodiode Detector
Sample Cuvette

## Slide 9
A Michelson Interferometer Uses Constructive/Destructive Interference
Slide 9
https://www.mpoweruk.com/figs/Michelson-Interferometer.htm
Constructive interference
Destructive interference
Shift ½ wavelength
d1
d2
d1 = d2
d1 = d2 - ½ λ
What happens if we start moving one of the mirrors?
The frequency (cycles/s) of the switch between constructive/destructive
= mirror velocity * 1/λ
The Laser Interferometer Gravitational-Wave Observatory (LIGO) uses an interferometer that is 4 kilometers long to detect gravitational waves

## Slide 10
The Interferogram:
All Wavelengths Simultaneously
Slide 10
https://www.newport.com/n/introduction-to-ftir-spectroscopy
Each wavelength alternates between constructive & destructive interference
But in a different time sequence
An Interferogram is the result
Chart: 
 | 1.8415 | 1.9093 | 1.1411 | 0.2432 | 0.041076 | 0.72058 | 1.657 | 1.9894 | 1.4121 | 0.45598 | 9.7934e-06 | 0.46343 | 1.4202 | 1.9906 | 1.6503 | 0.7121 | 0.038603 | 0.24901 | 1.1499 | 1.9129 | 1.8367 | 0.99115 | 0.15378 | 0.094422 | 0.86765 | 1.7626 | 1.9564 | 1.2709 | 0.33637 | 0.011968 | 0.59596 | 1.5514 | 1.9999 | 1.5291 | 0.57182 | 0.0082211 | 0.35646 | 1.2964 | 1.9638 | 1.7451 | 0.84138 | 0.083478 | 0.16823 | 1.0177 | 1.8509 | 1.9018 | 1.1236 | 0.23175 | 0.046247 | 0.73763
λ1
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
 | 1.8415 | 1.9093 | 1.1411 | 0.2432 | 0.041076 | 0.72058 | 1.657 | 1.9894 | 1.4121 | 0.45598 | 9.7934e-06 | 0.46343 | 1.4202 | 1.9906 | 1.6503 | 0.7121 | 0.038603 | 0.24901 | 1.1499 | 1.9129 | 1.8367 | 0.99115 | 0.15378 | 0.094422 | 0.86765 | 1.7626 | 1.9564 | 1.2709 | 0.33637 | 0.011968 | 0.59596 | 1.5514 | 1.9999 | 1.5291 | 0.57182 | 0.0082211 | 0.35646 | 1.2964 | 1.9638 | 1.7451 | 0.84138 | 0.083478 | 0.16823 | 1.0177 | 1.8509 | 1.9018 | 1.1236 | 0.23175 | 0.046247 | 0.73763
 | 1.3894 | 1.7174 | 1.932 | 1.9996 | 1.9093 | 1.6755 | 1.335 | 0.94163 | 0.55748 | 0.2432 | 0.048398 | 0.0038354 | 0.11655 | 0.36873 | 0.72058 | 1.1165 | 1.4941 | 1.7937 | 1.9679 | 1.9894 | 1.8546 | 1.5849 | 1.2229 | 0.82567 | 0.45598 | 0.17217 | 0.019064 | 0.020822 | 0.17717 | 0.46343 | 0.8344 | 1.2315 | 1.5921 | 1.8592 | 1.9906 | 1.9657 | 1.7883 | 1.4864 | 1.1078 | 0.7121 | 0.36189 | 0.11243 | 0.0030999 | 0.051156 | 0.24901 | 0.56543 | 0.95046 | 1.3433 | 1.682 | 1.9129
λ1 & λ2
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50
 | 3.2309 | 3.6267 | 3.0732 | 2.2428 | 1.9504 | 2.396 | 2.992 | 2.931 | 1.9696 | 0.69918 | 0.048408 | 0.46726 | 1.5367 | 2.3593 | 2.3709 | 1.8286 | 1.5327 | 2.0427 | 3.1178 | 3.9023 | 3.6913 | 2.5761 | 1.3767 | 0.92009 | 1.3236 | 1.9347 | 1.9754 | 1.2917 | 0.51354 | 0.4754 | 1.4304 | 2.7829 | 3.592 | 3.3882 | 2.5624 | 1.9739 | 2.1447 | 2.7828 | 3.0715 | 2.4572 | 1.2033 | 0.19591 | 0.17133 | 1.0689 | 2.0999 | 2.4672 | 2.074 | 1.5751 | 1.7282 | 2.6506
What the detector sees
λ1 + λ2

## Slide 11
Interferogram is Time Domain
Spectra is Frequency Domain
Slide 11
https://www.newport.com/n/introduction-to-ftir-spectroscopy
How do we get from an Interferogram in the time domain
To a spectra in the frequency domain?
Fourier transform math
f(frequency) = f(time)

f(ν) = f(t)e dt
∫
∞
∞
-
+
−i2πνt

## Slide 12
IR Sources are “Planck Black Body Radiators”
Slide 12
Do not all fix’d Bodies, when heated beyond a certain degree, emit Light and shine; and is not this Emission perform’d by the vibrating motion of its parts?
Without thinking, which is hotter?
Red hot or white hot?
What temperature range would give us photons in the mid-IR range?
Nernst Glower: heated rare earth oxide ~1500 K
Spectra output 1-50 um
Globar: heated silicon carbide ~1500 K
Spectra output 1-50 um
Isaac Newton, Opticks, published 1704.

## Slide 13
IR Detectors
Slide 13
“Pyroelectric” detectors –deuterated triglycine sulfate detector (DTGS) - work based on temperature differences
Visible photons are energetic and in semi-conductors will kick electrons out of valence bands and into conduction bands, producing a current
Mercury Cadmium Telluride (MCT) is an IR photon sensitive semiconductor which must be liquid N2 cooled
D* is a measure of sensitivity

## Slide 14
n1
n2
Refractive Index
Slide 14
The speed of light a constant 3.00 x 108 m/s
Slower in denser material
Concentration | Index
10% Glucose solution in water | 1.3477
20% Glucose solution in water | 1.3635
60% Glucose solution in water | 1.4394
n1 > n2
Fiber optics
θ1
θ2
θ1
θ2
θ1
Critical Angle
Refractive index n = c = speed in a vacuum
v speed in media
vacuum n = 1
water n = 1.33
Snell’s Law
n1 = sin θ2
n2 sin θ1
 in a vacuum
Refractive index is related to density

## Slide 15
Refractometry and Instrument Design
Slide 15
Visible
http://www.refractometer.pl/Abbe-refractometer